D2DMH OMNeT++ Short Documentation (Code is commented)

-D2DMH combines SimuLTE with routing in Inet Framework
-Following steps were made
- Binder needs to enable D2D capability between all UEs
-set utilizeAODV=true in module binder
-Mac addresses are needed to enable routing
-set utilizeAODV=true in mac module (LTEMacUE)
-IP2LTE module can note handle ARP
- set ARP module = GlobalARP in omnetpp.ini
-IP2LTE needs to handle IP packets differently. Packet’s next hop are in the control info	and not in the direct header anymore. Broadcast IPs are mapped to multicast IPs.
- set utilizeAODV=true in IP2LTE module
-Important change in LteMacUeD2D::macHandleRac

... if (racD2DMulticastRequested_)
      {
        bsrD2DMulticastTriggered_=true;
        bsrTriggered_=false; //ADDED

      }
      else
       {
        bsrTriggered_ = true
        bsrD2DMulticastTriggered_=false; //ADDED
      }
...
-Lines with “//ADDED” were added to handle multicast and unicast packets in one	simulation

- In LTERealisticChannelModel: Unit disc path loss model implemented
(Zero_Until_Tx_Range) --> Attenuation is zero until Tx_Range, inf for larger
-Necessary because implemented models have a maximum transmission range (10000m)
and neighbor discovery module only relies on distance and transmission range.
-Transmission range to be set in “config_channel.xml”

-AODV/LD
-Link Duration Module contained in every UE and contains following 3 submodules
-SimpleNeighborDiscovery: Responsible to determine if UE is reachable or not by	comparing Euclidean distance with transmission range. Emits a signal for AODV/LD
when link is broken
Is called every X seconds (could be adapted by parameter, default = 1s) → updates
NeighborLinkTimeTable
-NeighborLinkTimeTable: Contains information if and for how long UEs are neighbor of this	UE and is able to offer it
-ResidualLinkLifetime: Takes information of link lifetime distribution from CDF module and
link lifetime of NeighborLinkTimeTable to estimate residual link lifetime

-CDF module
-One module in whole simulation. Has information about Medina’s PDF and CDF
and is able to offer it
-Contains mapping from CDF(t)-> t, because inversion of CDF is complex to calculate
- Maximum for t is 24h (CDF(>24h) → CDF(24h))

AODVLDControlPackets_m
-Added residual link lifetime to RREQ
-Added residual route lifetime to RREP
-AODVLDRouting
-Minor adaption from AODV are commented in the code
-Still no route repair implemented
-Intermediate nodes are not allowed to send RREP, when they have a route to dest
- prehandleRREQ: RREQ are saved until a certain time, when new RREQ occur, it is
compared to previously transmitted RREQ and the best RREQ which is candidate for rebroadcasting at the moment. New RREQ is exchanged with the currently best one, when it is better than both.
-handle RREQ: Timer expired and the best RREQ is rebroadcasted
-Only RERR lead to invalidation of routes
- RRL = min(RLL), RLL taken from RREQs → adaption needed for better RRL estimation